## Slide 1
Terahertz (THz) technology offers a promising solution for non-contact vital sign monitoring, given its ability to detect subtle vibrations with high resolution. This project explores the application of a Terahertz (THz) interferometry setup for vibration sensing. The THz band's superior resolution for detecting subtle sound vibrations, compared to RF frequencies, makes it ideal for this application. Furthermore, THz systems operate at significantly lower power levels than optical sensors and can penetrate a wide range of common, optically opaque materials like clothing and plastic, overcoming the primary limitations of current optical-based methods.
Introduction
Materials & Methods

## Slide 2: THz Sensors for Vital Sign Monitoring Text for intro section (we can cut if necessary but can prob just cut it later after they give feedback)
THz(Terahertz) technology offers a promising solution for non-contact vital sign monitoring, given its ability to detect subtle vibrations with high resolution. This project explores the application of a Terahertz (THz) interferometry setup for vibration sensing. The THz band's superior resolution for detecting subtle sound vibrations, compared to RF frequencies, makes it ideal for this application. Furthermore, THz systems operate at significantly lower power levels than optical sensors and can penetrate a wide range of common, optically opaque materials like clothing and plastic, overcoming the primary limitations of current optical-based methods.
  Mention main advantage is DC power consumption is lower
Interferometry, as employed in this work, allows for high-resolution measurements by transforming phase information from reflected beams into amplitude modulation, which can then be captured by a detector. This method is particularly advantageous as it is not limited by phase noise, provided the phase noise of the two beams remains correlated over a small path difference [insert paper in brackets (the paper about interferometry]. The system utilizes a custom-designed THz Continuous Wave (CW) radiator chip, enabling the detection of sub-micrometer vibrations. This approach aims to demonstrate the potential of THz interferometry for accurate and non-invasive vital sign monitoring.

## Slide 3: Text for materials and methods section
The experimental configuration began with the THz waves from the CW radiator chip being collimated by an Off-Axis Parabolic (OAP) mirror. A beam splitter was used to divide the collimated beam into two separate paths. One beam was directed to a stationary plane mirror (M1), creating a reference arm. The second beam was directed to another plane mirror (M2), which was vibrated mechancially, which was vibrated by mechanical sound waves generated from a speaker, creating the target arm.
The reflected beams from both mirrors were recombined and focused onto the receiver, a VDI SAX module. The interference of the two beams converted the phase modulation from the vibrating target mirror into an amplitude-modulated signal. The intermediate frequency (IF) signal from the receiver was then amplified by low-noise baseband amplifiers. A power detector was used to measure the intensity of the resulting signal, and the output voltage was recorded by an oscilloscope. For maximum sensitivity, the vibrating mirror (M2) was physically positioned in a "sensitive region" where the detected voltage showed the highest slope with respect to the mirror's position.
  Must eventually mention frequency of wave and frequency of vibration (what the actual frequency is)

## Slide 4: References
Acknowledgements
We would like to express our sincere gratitude to our graduate student mentor, Benyamin Fallahi Motlagh, for his invaluable guidance, leadership, and support throughout the experimental and research phases of this project. We also thank Professor Aydin Babakhani for providing the opportunity to work in his laboratory. This work was supported by the National Science Foundation (NSF) under the Future of Semiconductors initiative.
Title: THz Sensors for Vital Sign Monitoring